## Slide 1: Registration methods and results
Pronoma Banerjee

## Slide 2: SimpleITK

## Slide 3: Rigid registration (CT)
Metric: Mattes Mutual Information
Optimizer: Gradient Descent
Final metric value: -0.6278285169931812
Multimodal

## Slide 4: Rigid registration (MRI)
Metric: Mattes Mutual Information
Optimizer: Gradient Descent
Final metric value: -0.46402962304107437
Multimodal

## Slide 5: Rigid registration
Similarity metric, mutual information (Mattes MI):
  Number of histogram bins, 50.
  Sampling strategy, random.
  Sampling percentage, 1%.
Interpolator, sitkLinear.
Optimizer, gradient descent:
  Learning rate, step size along traversal direction in parameter space, 1.0 .
  Number of iterations, maximal number of iterations, 100.
  Convergence minimum value, value used for convergence checking in conjunction with the energy profile of the similarity metric that is estimated in the given window size, 1e-6.
  Convergence window size, number of values of the similarity metric which are used to estimate the energy profile of the similarity metric, 10.

## Slide 6: Classic demons
Number Of Iterations: 50 RMS: 0.20766015075852373

## Slide 7: Classic demons
Implementation of the simple Demons algorithm by Thirion.
User supplied parameters: Number of iterations, Standard deviation of the Gaussian smoothing over the total displacement field.
Underlying assumption of the Demons framework: intensities of the homologous points are equal. The algorithm uses histogram matching to make the two images similar in intensities prior to registration.
The default interpolator used by simple ITK is Linear Interpolator.
(Thirion, J-P. "Image matching as a diffusion process: an analogy with Maxwell's demons." Medical image analysis 2.3 (1998): 243-260.)

## Slide 8: Diffeomorphic demons
Number Of Iterations: 50 RMS: 0.21839280684644166

## Slide 9: Diffeomorphic demons
A transformation function is a diffeomorphism if it is invertible and if both the function and its inverse is differentiable.
The demons algorithm can be seen as an optimization procedure on the entire space of displacement fields. The main idea of this algorithm is to adapt this procedure to a space of diffeomorphic transformations.
(Vercauteren, Tom, et al. "Non-parametric diffeomorphic image registration with the demons algorithm." International Conference on Medical Image Computing and Computer-Assisted Intervention. Springer, Berlin, Heidelberg, 2007.)

## Slide 10: Fast symmetric forces demons
Number Of Iterations: 50 RMS: 0.21884685178865218

## Slide 11: Symmetric forces demons
Number Of Iterations: 50 RMS: 0.5223684369785287

## Slide 12: Symmetric forces demons
Algorithm is symmetric with respect to the order of input images.

## Slide 13: BSpline1 Registration
Metric: Mattes Mutual Information
Optimizer: Gradient Descent Line Search
Multimodal

## Slide 14: BSpline1 Registration
Deformable transform of points from one N-dimensional space to another N-dimensional space. The deformation field is modelled using B-splines.
A deformation is defined on a sparse regular grid of control points and is varied by defining a deformation of each control point. The deformation at any point is obtained by using a B-spline interpolation kernel.
A BSpline transform usually has a large number of parameters which increases the complexity and duration of optimizing the deformation.
The deformation field grid is defined by a user specified GridRegion, GridSpacing and GridOrigin. Each grid/control point has associated with it N deformation coefficients , representing the N directional components of the deformation. Deformation outside the grid plus support region for the BSpline interpolation is assumed to be zero.
The parameters for this transform is an N x N-D grid of spline coefficients. The user specifies the parameters as one flat array: each N-D grid is represented by an array in the same way an N-D image is represented in the buffer; the N arrays are then concatenated together on form a single array.

## Slide 15: BSpline1 Registration
The algorithm used here is designed for multi-modal image registration. The multi-resolution framework uses two methods, SetShrinkFactorsPerLevel and SetSmoothingSigmasPerLevel. The former receives the shrink factors to apply when moving from one level of the pyramid to the next and the later receives the sigmas to use for smoothing when moving from level to level.
Mattes Mutual Information: Joint Probability density distribution are estimated using Parzen histograms. This gives a quantitative measure of how similar the images are. High mutual information implies a large reduction in the uncertainty (entropy) between the two distributions, signalling that the images are likely better aligned.
The Mattes mutual information algorithm uses a single set of pixel locations for the duration of the optimization, instead of drawing a new set at each iteration.
Zero-order and third-order B-spline kernels are used to compute the probability density functions of the fixed and moving images, respectively.

## Slide 16: BSpline2 Registration
Metric: Joint Histogram Mutual Information
Optimizer: Gradient Descent Line Search
Multimodal

## Slide 17: BSpline2 Registration
All parameters are same as BSpline1 Registration, except that it uses Joint Histogram Mutual Information, which calculates the mutual information between two histograms.
Mutual Information is defined as:

## Slide 18: Displacement field transform
Metric: Joint Histogram Mutual Information & ANTS Neighborhood Correlation
Optimizer: Gradient Descent
MI metric value: -5.888361371624239
Correlation: -0.13062562413990564
Iterations: 30
Multimodal?

## Slide 19: Displacement field transform
Has 2 stages of registration. The first stage uses Joint Histogram Mutual Information, whereas second stage uses ANTS Neighborhood Correlation, both stages use Gradient Descent Optimization.
Provides local/dense/high-dimensionality transformation via a displacement field. The displacement field stores vectors of displacements, with dimension NDimensions. Transformation is performed at a given point by adding the displacement at that point to the input point.
T(x, p), x is the position, p is the local parameter at position x. For a 2D example, if
x = (x0, x1), p = (p0, p1), then T(x, p) is defined as: T(x, p)=(T0, T1)=(x0+p0,x1+p1).

## Slide 20: Exhaustive MI Registration
Metric: Mattes Mutual Information
Optimizer: Exhaustive
Multimodal

## Slide 21: Exhaustive MI Registration
3D rigid registration with the Exhaustive Optimizer
Because gradient descent base optimization can get stuck in local minima, a good initial transform is critical for reasonable results. Search a reasonable space on a grid with brute force may be a reliable way to get a starting location for further optimization.
The initial translation and center of rotation for the transform is initialized based on the first principle moments of the intensities of the image. Then in either 2D or 3D a Euler transform is used to exhaustively search a grid of the rotation space at a certain step size.

## Slide 22: Elastix + ITK

## Slide 23: Rigid Registration (MRI)
Optimizer: Stochastic gradient descent
Metric: Mutual information
Multimodal

## Slide 24: Rigid Registration (CT)
Optimizer: Gradient descent, stochastic gradient descent
Metric: Mutual information

## Slide 25: BSpline Registration
Rigid+BSpline registration
Intensity based
Optimizer: Stochastic gradient descent
Metric: Mutual information

## Slide 26: BSpline Registration
The method is based on a 3D or 4D free-form B-spline deformation model, a similarity metric that minimizes the intensity variances over time and constrained optimization using a stochastic gradient descent method with adaptive step size estimation.
(Metz, Coert T., et al. "Nonrigid registration of dynamic medical imaging data using nD+ t B-splines and a groupwise optimization approach." Medical image analysis 15.2 (2011): 238-249.)
Click to add text

## Slide 27: MITK

## Slide 28: Fast symmetric forces demons
Monomodal registration
Metric: Mean square

## Slide 29: Level-set motion
Monomodal registration
Metric: Mean square